## Slide 1
ASSIGNMENT 2 · TECHNOLOGY DEEP DIVE
Solid-state batteries: the next leap in storage
Swap the flammable liquid electrolyte for a solid one — unlocking energy density, safety and fast charge.
HOW IT WORKS — Li-ion vs. solid-state cell
CONVENTIONAL Li-ION
Cathode
Liquid electrolyte
+ porous separator
Graphite
anode
flammable · ~250–300 Wh/kg
SOLID-STATE
Cathode
Solid electrolyte
(also the separator)
Li-metal /
anode-free
non-flammable · ~2× density
The solid electrolyte conducts lithium ions while physically blocking dendrites — so it can pair with a high-capacity lithium-metal (or anode-free) design that liquid cells cannot safely use.
WHY IT MATTERS
Energy density — ~2× — longer range or smaller, lighter packs
Safety — No flammable liquid → far lower fire/thermal-runaway risk
Fast charge — High-rate charging with less degradation
Supply-chain edge — Anode-free designs cut graphite (China-dominated)
THE ELECTROLYTE FAMILIES
Sulfides: Highest conductivity, but moisture-sensitive — Toyota, Samsung, Solid Power
Oxides (e.g. LLZO): Stable & safe, but brittle & high-temp to process — QuantumScape, ProLogium
Polymers / halides: Flexible or emerging; lower room-temp conductivity
Solid-State Batteries · Technology Deep Dive
01 / 05

## Slide 2
STATE OF THE ART (GLOBAL)
From the lab to the first cells on the road
800+
Wh/L — QuantumScape QSE-5 (vs ~700 for top Li-ion)
~12 min
10→80% fast charge demonstrated
400→700+
km EV range at equal pack mass
>99.5%
coulombic efficiency; <2%/mo self-discharge
WHERE THE FIELD ACTUALLY IS (2025–26)
Validated chemistry — Anode-free lithium-metal and semi-solid cells now cycle at automotive-relevant rates and sizes.
On real vehicles — QuantumScape QSE-5 B-sample cells shipped to OEMs in 2025; demoed on Ducati / Verge motorbikes.
Pilot lines live — QS 'Cobra' separator + 'Eagle' pilot line; Solid Power & others running pre-pilot lines.
Supply chains forming — Toyota–Idemitsu (~$142M sulfide plant, 2027–28) and QS–Murata (ceramic separator) lock in materials.
Reality check
These are sample and pilot volumes — not gigascale.
No all-solid-state EV is yet in mass production. The gap from a working cell to millions of cheap, reliable, identical cells is the whole game — and semi-solid (quasi-solid) cells, which keep some liquid, will reach cars first.
Solid-State Batteries · Technology Deep Dive
02 / 05

## Slide 3
KEY PLAYERS — GLOBAL & INDIA
The US and Asia lead; India is still at the lab bench
GLOBAL FRONTRUNNERS
Player (HQ)
Approach
Status / backing
QuantumScape (US)
Anode-free Li-metal + oxide ceramic separator
QSE-5 B-samples; VW / PowerCo; Murata
Toyota (JP)
Sulfide electrolyte
Mass production targeted 2027–28; Idemitsu
Samsung SDI (KR)
Sulfide, high-Ni
Pilot; ~2027 premium-EV target
Solid Power (US)
Sulfide; licensing model
BMW & Ford partnerships; pre-pilot line
Factorial (US)
Semi-solid (quasi-solid)
Mercedes & Stellantis; cells in test fleets
ProLogium (TW)
All-inorganic oxide / ceramic
Giga plant in France; FAW, Mercedes
CATL / BYD (CN)
Condensed / semi-solid + LMB R&D
Scale incumbents; aggressive roadmaps
India: nascent
No commercial SSB cell maker yet
India has no domestic all-solid-state production; effort is overwhelmingly R&D-stage.
Corporates with SSB on the roadmap
GODI India lists all-solid-state among its cell programmes; large players watch, none ship.
Public research base
ARCI (Hyderabad), IISc, several IITs and CSIR labs work on solid electrolytes & Li-metal.
The pragmatic indigenous bet
Sodium-ion (Indi Energy, Rechargion) is far closer to market for India than SSB — a better near-term leapfrog.
Solid-State Batteries · Technology Deep Dive
03 / 05

## Slide 4
KEY TECHNICAL BOTTLENECKS
Why it isn't on every car yet
Solid–solid interfaces
Unlike a liquid that wets everything, a rigid electrolyte makes poor contact with electrodes — raising resistance and degrading as the cell cycles.
Dendrites at high current
Lithium can still nucleate and crack through the electrolyte during fast charge, eventually shorting the cell.
Pressure & brittleness
Many cells need steady mechanical pressure (atmospheres) to stay in contact; ceramics are brittle and crack under stress and cycling.
Moisture-sensitive sulfides
The most conductive electrolytes react with air/water, forcing inert, dry-room handling that complicates manufacturing.
Manufacturing at scale
Producing thin, defect-free electrolyte layers and stacking them fast, cheaply and identically — by the million — is unproven at gigascale.
Cost
Lithium-metal handling, exotic materials and new process equipment keep $/kWh well above mature lithium-ion today.
Solid-State Batteries · Technology Deep Dive
04 / 05

## Slide 5
TIMING & THE INDIA ANGLE
Commercialisation horizon — and where India can play
COMMERCIALISATION TIMELINE
2025–27
Niche & high-value
Consumer electronics, motorsport, eVTOL, defence/aerospace, AI-datacentre racks; semi-solid first.
2027–30
Premium EVs
Toyota / Samsung / QS target premium models; semi-solid scales; early gigalines ramp.
2030+
Mainstream & grid
Cost-down toward mass-market EVs and, eventually, selective stationary-storage use.
INVESTMENT OPPORTUNITIES IN INDIA
Materials & components
Solid electrolytes (sulfide/oxide), Li-metal anodes, separators, hard carbon — sell into the global supply chain.
Manufacturing & equipment
Dry-room handling, thin-film coating and stacking know-how — the picks-and-shovels of cell-making.
Selective deep-tech bets
A few cell-innovation teams (e.g. e-TRNL's 3DEA, GODI) and IP/licensing or academic spin-outs.
Sodium-ion as the leapfrog
Back the nearer-term indigenous play now; keep optionality on SSB for the 2030s.
India's smart bet: components + sodium-ion now, with venture optionality on a few cell-innovation teams — not a domestic solid-state champion just yet.
Solid-State Batteries · Technology Deep Dive
05 / 05